## Slide 1: THE EVOLUTION OF THE INTEL X86 AND ARM ARCHITECTURE
21/U/05662/EVE
KASASIRA CHARLES DERRICK
kasasira.charles@students.mak.ac.ug

## Slide 2: INTEL X86 ARCHITECTURE
Intel x86 is a family of Complex Instruction Set architectures (CISC) developed by Intel. Intel x86 architecture has evolved over the years. From a 29, 000 transistors microprocessor 8086 that was the first introduced to a quad core Intel core 2 which contains 820 million transistors, the organisation and technology has changed dramatically.

## Slide 3: Some of the highlights of evolution of x86 architecture are:
8080 – The world’s first general purpose microprocessor. It was an 8-bit machine, with an 8-bit data path to memory.
8086 – It was a 16-bit machine and was far more powerful than previous one. It had a wider data path of 16-bits and larger registers along with an instruction cache or queue that prefetches a few instructions before they are executed. It is the first appearance of 8086 architecture. It has a real mode and an addressable memory of 1 MB.
80286 – It has an addressable memory of 16 MB instead of just 1 MB and contains two modes-real mode and first generation 16-bit protected mode. It has a data transfer width of 16-bits and programming model of 16-bits (16-bits general purpose registers and 16-bit addressing).
80386 – It was Intel’s first 32-bit machine. Due to its 32-bit architecture it was able to compete against the complexity and power of microcomputers and mainframes introduced just a few years earlier. It was the first processor to support multitasking and contained the 32-bit protected mode. It also implemented the concept of paging (permitted 32-bit virtual memory address to be translated into 32-bit physical memory address). It has an addressable physical memory of 4 GB and data transfer width of 32-bits.

## Slide 4
80486 – It introduced the concept of cache technology and instruction pipelining. It contained write protect feature and offered a built in math co-processor that offloaded complex math operations from the main CPU.
Pentium – The use of superscalar techniques was introduced as multiple instructions started executing in parallel. The page size extension (PSE) feature was added as a minor enhancement in paging.
Pentium Pro – It used register renaming, branch prediction, data flow analysis, speculative execution and more pipeline stages. Advanced optimization techniques in microcode were also added along with level 2 cache. It implemented the second generation address translation in which 32-bit virtual address is translated into 36-bit physical memory address.
Pentium II – It was able to process video, audio and graphics data efficiently by incorporating Intel MMX technology (multimedia data set).
Pentium III – It contains SMD (streaming extensions) instructions (SSE) and supports 3D graphics software. It has a maximum CPU clock rate of 1.4 GHz and contained 70 new instructions.

## Slide 5
Pentium 4 – It implements third generation address translation that translates 48-bit virtual memory address to 48-bit physical memory address. It contains other floating point enhancements for multimedia.
Core – It is the first Intel microprocessor with dual core that is the implementation of 2 processors on a single chip. There is an addition of Visualizing Technology.
Core 2 – It extends the architecture to 64-bits and core 2 Quad provides four processors on a single chip. The register set as well as addressing modes are of 64-bits.

## Slide 6: ARM ARCHITECTURE
ARM (Advanced RISC Machines) is a family of instruction set architectures used in making computer processors. It is based on the Reduced Instruction Set Computing architecture which is commonly called as RISC. Some of the highlights of the arm architecture:
ARM1 This was the very first ARM processor and was very close in capabilities to the ARM2. This processor was used in a few evaluation systems for BBC and PC machines, but it was primarily a prototype chip and was superseded by the ARM2.
ARM2 The ARM2 chip features 27 registers of which 16 are accessible at any one time. Due to the top six bits of the program counter being used to hold the processor status flags this chip was restricted to addressing 26 bits of memory, or a 64 Megabyte address space.
ARM3
ARM4 & ARM5 These were never made. In the change over from Acorn to Armltd designing the processors the number scheme for the chips was changed. As such the numbers 4 and 5 were skipped.

## Slide 7
ARM6 This processor cell is the first of the commercially available ARMs to have a full 32bit addressing capability. Additionally the processor now has 31 registers in it along with six new processor modes
ARM7 The ARM7 cell is functionally identical to the ARM6 cell in capabilities but may be clocked faster than the ARM6. A variant of the ARM7 cell offers an improved hardware multiply, suitable for DSP work.
ARM8
StrongARM
ARM9
ARM10

## Slide 8: REFERENCES
Geeks for Geeks (01 August 2018) : https://www.geeksforgeeks.org/microprocessor-intel-x86-evolution-and-main-features/
ARM Architecture, Wikipedia: https://en.wikipedia.org/wiki/ARM_architecture