## Slide 1: CACHE MEMORY
21/U/05662/EVE
KASASIRA CHARLES DERRICK
kasasira.charles@students.mak.ac.ug

## Slide 2: What is Cache Memory
Cache Memory is a small-sized type of volatile computer memory that provides high-speed data access to a processor and stores frequently used computer programs, applications and data. It stores and retains data only until a computer is powered up.
The intent of cache memory is to provide the fastest access to resources without compromising on size and price of the memory. The processor attempting to read a byte of data, first looks at the cache memory. If the byte does not exist in cache memory, it searches for the byte in the main memory. Once the byte is found in the main memory, the block containing a fixed number of byte is read into the cache memory and then on to the processor.

## Slide 3: Working of Cache Memory
The CPU initially looks in the Cache for the data it needs
If the data is there, it will retrieve it and process it
If the data is not there, then the CPU accesses the system memory and then puts a copy of the new data in the cache before processing it.
Next time if the CPU needs to access the same data again, it will just retrieve the data from the cache instead of going through the whole loading process again

## Slide 4: Levels of Cache Memory
Level 1 (L1) Cache: this is the first cache and it usually comes within the processor chip itself, it typically ranges in size from 8kb to 64kb and uses high speed Static RAM
Level 2 (L2) Cache: this is larger but slower in speed than L1 cache, stores recently accessed information and is also know as secondary cache., it typically ranges in size from 64kb to 4mb
Level 3 (L3) Cache: this is an enhanced form of memory present on the motherboard of the computer, it is used to feed the L2 cache, and is typically faster than system’s main memory, but still slower than the L2 cache, having more than 3mb of storage in it.

## Slide 5: REFERENCES
Wikipedia www.wikipedia.org
Thinkquest.org